## Slide 1
DIGITIZING HAND-DRAWN LOGIC CIRCUITS USING COMPUTER VISION
Interim Project Review
Oshadha Naghawatte - S/21/444

## Slide 2
THE PROBLEM:
  Translating inconsistent, hand-drawn logic circuits into functional digital netlists using pure Computer Vision.
THE CHALLENGE OF HUMAN VARIANCE:
  Heavy ink and overlapping traces.
  Wobbly lines and imperfect geometry.
THE DATASET:
  A custom collection of hand-drawn circuits on paper, scaling from simple 2/3-gate topologies to complex structures.

## Slide 3
THE MULTI-STAGE IMAGE PROCESSING PIPELINE
Grayscale conversion, Median Blur, Gaussian Adaptive Thresholding.
STEP 1: PREPROCESSING
STEP 2: GAP SEALING & FLOOD FILL
Morphological closing to handle human variance in pen pressure.
STEP 3: ADVANCED SEGMENTATION
"Jaws of Life" Heavy-Duty Morphological Opening (35x35 kernel).

## Slide 4
DETERMINISTIC HEURISTIC CLASSIFICATION
Utilizing deterministic pure geometry rather than probabilistic machine learning models.
  Metric 1: Solidity: (Area / Convex Hull Area). Detects the complex "dent" in the back curve of an OR gate versus the solid block of an AND gate.
  Metric 2: Extent: (Area / Bounding Box Area). The ultimate "Triangle Trap." A triangle mathematically cannot fill its bounding box, instantly isolating NOT gates regardless of size.
  Generalization Success: High robustness against human variance in geometry, wobbly lines, and sizing.

## Slide 5
  Gate Masking: Erasing detected bounding boxes to isolate the raw, unconnected wire pixels.
FROM PIXELS TO LOGIC
NETLIST GENERATION
  Parsing the JSON Netlist to virtually rebuild the circuit geometry.
LOGIC EXECUTION
  Skeletonization: Applying morphological thinning to compress thick, wobbly hand-drawn traces into precise 1-pixel-wide paths.
  Graph Pathfinding: Treating gates as 'Nodes' and skeletonized wires as 'Edges' to map connections and export a structured JSON Netlist.
  Applying standard Boolean logic to automatically calculate and output the final Truth Table.
CURRENT STATUS :
A fully functional, end-to-end pipeline from physical paper to digital simulation.

## Slide 6
TECHNICAL CHALLENGES
  The Segmentation vs. Integrity Paradox: Weak morphological operations left interconnecting wires, creating "Giant Blobs." Stronger operations cleanly severed wires but "decapitated" tiny NOT gates, destroying their geometric signature.
  Solution: Developed a localized, surgical "Goldilocks scalpel" (13x13 elliptical opening) applied strictly within padded bounding boxes.
  Brittle Thresholding (Overfitting): Static limits (e.g., Solidity > 0.85 or specific corner counts) failed when human variance produced borderline geometry (e.g., a wobbly line registering as 8 corners).
  Solution: Pivoted to a multi-factored, deterministic decision tree where Extent acts as the ultimate "Triangle Tie-Breaker" rule.

## Slide 7
FUTURE SCOPE & REMAINING WORK
NEXT PHASE 1:
NEXT PHASE 2:
Expanding the Combinational Library
The Sequential Logic Leap
  Extending the geometric classifier to identify complex derived gates: NAND, NOR, XOR, and XNOR.
  Tuning the pipeline to handle extremely dense, tightly packed circuit diagrams.
  Moving beyond feed-forward combinational logic to detect circuits with state and memory.
  Identifying feedback loops and sequential elements like Latches and Flip-Flops (D, T, SR, JK).

## Slide 8
THANK YOU